## Slide 1
Asso. Prof. Dong Yabo
dongyb@zju.edu.cn
College of Computer Science and Technology, Zhejiang University

## Slide 2: Overview
Memory definitions
Random Access Memory (RAM)
Static RAM (SRAM) integrated circuits
  Cells and slices
  Cell arrays and coincident selection
Arrays of SRAM integrated circuits
Dynamic RAM (DRAM) integrated circuits
DRAM Types
  Synchronous (SDRAM)
  Double-Data Rate (DDR SRAM)
  RAMBUS DRAM (RDRAM)
Arrays of DRAM integrated circuits

## Slide 3: Memory Definitions
Memory ─ A collection of storage cells together with the necessary circuits to transfer information to and from them.
Memory Organization ─ the basic architectural structure of a memory in terms of how data is accessed.
Random Access Memory (RAM) ─ a memory organized such that data can be transferred to or from any cell (or collection of cells) in a time that is not dependent upon the particular cell selected.
Memory Address ─ A vector of bits that identifies a particular memory element (or collection of elements).

## Slide 4: Memory Definitions (Continued)
Typical data elements are:
  bit ─ a single binary digit
  byte ─ a collection of eight bits accessed together
  word ─ a collection of binary bits whose size is a typical unit of access for the memory. It is typically a power of two multiple of bytes (e.g., 1 byte, 2 bytes, 4 bytes, 8 bytes, etc.)
Memory Data ─ a bit or a collection of bits to be stored into or accessed from memory cells.
Memory Operations ─ operations on memory data supported by the memory unit. Typically, read and write operations over some data element (bit, byte, word, etc.).

## Slide 5: Memory Organization
Organized as an indexed array of words. Value of the index for each word is the memory address.
Often organized to fit the needs of a particular computer architecture. Some historically significant computer architectures and their associated memory organization:
  Digital Equipment Corporation PDP-8 – used a 12-bit address to address 4096 12-bit words.
  IBM 360 – used a 24-bit address to address 16,777,216 8-bit bytes, or 4,194,304 32-bit words.
  Intel 8080 – (8-bit predecessor to the 8086 and the current Intel processors) used a 16-bit address to address 65,536 8-bit bytes.
PDP-8
IBM 360
Intel 8080
Intel 8086
Notes: PDP-8：1964年生产，是第一台大规模生产的微处理机
Intel 8080：1974年4月，包含6000多个晶体管

## Slide 6: Memory Block Diagram
A basic memory system is shown here:
k address lines are decoded to address 2k words of memory.
Each word is n bits.
Read and Write are single control lines defining the simplest of memory operations.
n Data Input Lines
k Address Lines
Read
Write
n Data Output Lines
Memory
Unit
2k Words
n Bits per Word
k
1
1
n
n

## Slide 7: Memory Organization Example
Example memory contents:
  A memory with 3 address bits & 8 data bits has:
  k = 3 and n = 8 so 23 = 8 addresses labeled 0 to 7.
  23 = 8 words of 8-bit data
Memory Address |  | Memory Content
Binary | Decimal | 
000 | 0 | 1 0 0 0 1 1 1 1
001 | 1 | 1 1 1 1 1 1 1 1
010 | 2 | 1 0 1 1 0 0 0 1
011 | 3 | 0 0 0 0 0 0 0 0
100 | 4 | 1 0 1 1 1 0 0 1
101 | 5 | 1 0 0 0 0 1 1 0
110 | 6 | 0 0 1 1 0 0 1 1
111 | 7 | 1 1 0 0 1 1 0 0

## Slide 8: Basic Memory Operations
Memory operations require the following:
  Data ─ data written to, or read from, memory as required by the operation.
  Address ─ specifies the memory location to operate on. The address lines carry this information into the memory. Typically: n bits specify locations of 2n words.
  An operation ─ Information sent to the memory and interpreted as control information which specifies the type of operation to be performed. Typical operations are READ and WRITE. Others are READ followed by WRITE and a variety of operations associated with delivering blocks of data. Operation signals may also specify timing info.

## Slide 9: Basic Memory Operations (continued)
Read Memory ─ an operation that reads a data value stored in memory:
  Place a valid address on the address lines.
  Toggle the memory read control line.
  Wait for the read data to become stable.
Write Memory ─ an operation that writes a data value to memory:
  Place a valid address on the address lines and valid data on the data lines.
  Toggle the memory write control line.
Sometimes the read or write enable line is defined as a clock with precise timing information (e.g. Read Clock, Write Strobe).
  Otherwise, it is just an interface signal.
  Sometimes memory must acknowledge that it has completed the operation.

## Slide 10: Memory Operation Timing
Most basic memories are asynchronous
  Storage in latches or storage of electrical charge
  No clock
Controlled by control inputs and address
Timing of signal changes and data observation is critical to the operation
Read timing:
Read cycle 读取延迟
Clock
Address
Memory
enable
Read/
Write
Data
output
20 ns
T1
T2
T3
T4
T1
Address valid
65 ns
Data valid

## Slide 11: Memory Operation Timing
Write timing:
Critical times measured with respect to edges of write pulse (1-0-1):
  Address must be established at least a specified time before 1-0 and held for at least a specified time after 0-1 to avoid disturbing stored contents of other addresses
  Data must be established at least a specified time before 0-1 and held for at least a specified time after 0-1 to write correctly
Write cycle
Clock
Address
Memory
enable
Read/
Write
Data
input
20 ns
T1
T2
T3
T4
T1
Address valid
Data valid
75 ns
Notes: CPU控制Read/Write
CPU提供数据到Data input
Read/Write拉高表示读取完成，Data在input上多保持一会，防止没读上

## Slide 12: RAM Integrated Circuits
Types of random access memory
  Static – information stored in latches
  Dynamic – information stored as electrical charges on capacitors
    Charge “leaks” off
    Periodic refresh of charge required
Dependence on Power Supply
  Volatile – loses stored information when power turned off
  Non-volatile – retains information when power turned off
Notes: SRAM静态存储器，信息保持在Latch中，每一位对应一套Latch
优点是由于Latch用门存储，所以速度快，但是一个bit存储需要8个以上晶体管，成本较大，存储密度低，集成度低，面积大
DRAM使用电容存储，但是一段时间后电容放电会导致数据消失，所以需要定时刷新
集成密度高，成本低

## Slide 13: Static RAM － Cell
Array of storage cells used to implement static RAM
Storage Cell
  SR Latch
  Select input for control
  Dual Rail Data Inputs B and B
  Dual Rail Data Outputs C and C
Select
B
RAM cell
C
C
B
S
R
Q
Q

## Slide 14: Static RAM － Bit Slice
Represents all circuitry that is required for 2n 1-bit words
  Multiple RAM cells
  Control Lines:
    Word select i – one for each word
    Bit Select
  Data Lines:
    Data in
    Data out
(a) Logic diagram
Select
S
R
Q
Q
B
RAM cell
C
C
B
Select
W
ord
select
2
n
-
1
W
ord
select
2
n
-
1
W
ord
select
0
W
ord
select
1
S
R
Q
Q
RAM cell
X
W
ord
select
0
Data in
Write logic
Bit
select
S
R
Q
Q
X
X
X
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
(b) Symbol
RAM cell
RAM cell
RAM cell
Data out
Read logic
Write
Read/
Notes: Read/Write 为0是写入，为1是读取
在任何时刻最多只有一个word select是1，其他都是0，需要使用decoder来控制word select

## Slide 15: 2n-Word  1-Bit RAM IC
Read/
To build a RAM IC from a RAM slice, we need:
  Decoder － decodes the n address lines to 2n word select lines
  A 3-state buffer on the data output permits RAM ICs to be combined into a RAM with c  2n words
Word select
Read/Write
logic
Data in
Data out
Write
Bit
select
(b) Block diagram
RAM cell
RAM cel
l
RAM cell
Data input
Chip select
Read/Write
Data
output
A
3
A
2
A
1
A
0
2
3
2
2
2
1
2
0
4-to-16
Decoder
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
A
3
A
2
A
1
A
0
Data
input
Data
output
(a) Symbol
Read/
Write
Memory
enable
16 x
1
RAM

## Slide 16: Cell Arrays and Coincident Selection
Memory arrays can be very large =>
  Large decoders
  Large fanouts for the bit lines
  The decoder size and fanouts can be reduced by approximately by using a coincident selection in a 2-dimensional array
  Uses two decoders, one for words and one for bits
  Word select becomes Row select
  Bit select becomes Column select
See next slide for example
  A3 and A2 used for Row select
  A1 and A0 for Column select

## Slide 17: Cell Arrays and Coincident Selection (continued)
Data input
Read/Write
X
X
X
A
1
A
0
RAM cell
0
RAM cell
4
RAM cell
8
RAM cell
12
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
RAM cell
1
RAM cell
5
RAM cell
9
RAM cell
13
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
RAM cell
2
RAM cell
6
RAM cell
10
RAM cell
14
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
RAM cell
3
RAM cell
7
RAM cell
11
RAM cell
15
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
Column
decoder
2-to-4 Decoder
with enable
2
1
2
0
0
1
Column select
2
Enable
3
Chip select
Data
output
Row
select
Row decoder
A
2
A
3
X
2-to-4
Decoder
2
0
2
1
1
2
3
0
Notes: 高位 A2 A3 行地址，低位列地址
A0 A1 A2 A3 = 1001 对应RAM cell9
同样任何时候只有一个位片是被是能的
这是16*1

## Slide 18: RAM ICs with > 1 Bit/Word
Word length can be quite high.
To better balance the number of words and word length, use ICs with > 1 bit/word
See Figure in next slide for example
  2 Data input bits
  2 Data output bits
  Row select selects 4 rows
  Column select selects 2 pairs of columns

## Slide 19
8×2RAM
Notes: 由两个位片组成一个字
蓝线低位绿线高位

## Slide 20: Making Larger Memories
Using the CS lines, we can make larger memories from smaller ones by tying all address, data, and R/W lines in parallel, and using the decoded higher order address bits to control CS.
Using the 4-Word by 1-Bit memory from before, we construct a 16-Word by 1-Bit memory. 
Notes: 每个小芯片有A0 A1两个地址线，是4 * N的芯片，四个连一起形成16*N芯片
A0 A1 A2 A3 = 1001，从上到下第二个芯片被使能，内部的01号地址被使能，此处存储的数据被输出
没有被使能的芯片输出是高阻态，所以Data out被接在一起

## Slide 21: 64K×8RAM

## Slide 22: Using 64K×8RAM construct 256K×8RAM

## Slide 23: Making Wider Memories
To construct wider memories from narrow ones, we tie the address and control lines in parallel and keep the data lines separate.
For example, to make a 4-word by 4-bit memory from 4, 4-word by 1-bit memories 
Note: Both 16x1 and 4x4 memories take 4-chips and hold 16 bits of data.

## Slide 24: Using 64K×8RAM construct 64K×16RAM
Notes: 一个芯片输出当高字节，一个当低字节

## Slide 25: SRAM For SWORD：CY7C1061DV33
16-Mbit(1M×16) Static
220=1M WORD
Word=16bit
Notes: 3片，1M×16b
SWORD-V2版(紫金港)：BHE/BLE、OE、WE、CE1/CE2信号三个芯片6Byte同时控制。影响写操作，需读回写。
SWORD-V4版(玉泉)：BHE/BLE、OE、WE、CE1/CE2信号3个芯片6B可分别控制。可分别写。

## Slide 26: SWORD Onboard memory-SRAM
Memory Organization：
  CY7C1061DV33×3 for 1M×48bit(6MB)

## Slide 27: Other Memory for SWORD-NOR Flash
S29GL128S10TFI010
128 Mbit
8M*16bit
223=8M Word
A22 ~ A0
Word = 16bit

## Slide 28: SWORD Onboard memory-NOR Flash
Memory Organization：
  S29GL128S10TFI010×2 for 8M×32bit(32MB)
读写时序不同请查阅手册

## Slide 29: Dynamic RAM (DRAM)
Basic Principle: Storage of information on capacitors.
Charge and discharge of capacitor to change stored value
Use of transistor as “switch” to:
  Store charge
  Charge or discharge
See next slide for circuit, hydraulic analogy, and logical model.

## Slide 30: Dynamic RAM (continued)
(a)
(c)
Select
D
C
Q
B
DRAM cell
model
C
(f)
(g)
(h)
Select
B
T
C
DRAM cell
To Pump
(b)
(d)
(e)
Stored 1
Stored 0
Write 1
Write 0
Read 1
Read 0
Notes: Warning: (d), (e), (f), and (g) are animated. Each animation is triggered with a mouse click
and goes through two steps at 1 second intervals.
左边是大电容，右边是小电容，若干小电容接在一个大电容，晶体管式开关

## Slide 31: Dynamic RAM - Bit Slice
C is driven by 3-state drivers
Sense amplifier is used to change the small voltage change on C into H or L
In the electronics, B, C, and the sense amplifier output are connected to make destructive read into non-destructive read
(b) Symbol
(a) Logic diagram
Select
B
Select
W
ord
select
0
Data in
Write logic
Bit
select
Data out
Read logic
D
C
Q
DRAM cell
model
D
C
Q
DRAM cell
model
C
Sense
amplifier
Read/Write
logic
Data in
Data out
Bit
select
DRAM cell
DRAM cell
DRAM cell
W
ord
select
0
W
ord
select
1
Read/
Write
Read/
Write
2n -1
2n -1
Word
select
Word
select

## Slide 32: Dynamic RAM - Block Diagram
Block Diagram – See next slide
Refresh Controller and Refresh Counter
Read and Write Operations
  Application of row address:
  Application of column address:
  Why is the address split?
  Why is the row address applied first?
Notes: The address is split to roughly halve the large number of address pins on the typical RAM IC.
The row address is used to select the row of cells to be read within the memory.
The column address is used to select the word to be placed on the output from the data read
from the row of cells. Since the data must be read from the cells before it can be selected, the
row address must be applied first.
DRAM的储存量很大因此输入引脚比较多，需要分两次来送地址，先行后列

## Slide 33: Dynamic RAM - Block Diagram
Notes: The address is split to roughly halve the large number of address pins on the typical RAM IC.
The row address is used to select the row of cells to be read within the memory.
The column address is used to select the word to be placed on the output from the data read
from the row of cells. Since the data must be read from the cells before it can be selected, the
row address must be applied first.

## Slide 34: Dynamic RAM Read Timing
Read cycle
20 ns
T1
T2
T3
T4
T1
Data valid
65 ns
Hi-Z
Read/
Write
Data
output
Clock
Row
Address
Column
Address
RAS
CAS
Address
Output
enable
Notes: CPU先提供行地址，RAS标记为下降沿，再送过去一个列地址，CAS为下降沿】
行地址是个寄存器，列地址是个计数器

## Slide 35: Dynamic RAM Write Timing
Write cycle
20 ns
T1
T2
T3
T4
T1
75 ns
Read/
Write
Data
input
Clock
Row
Address
Column
Address
RAS
CAS
Address
Output
enable
Data valid

## Slide 36: DRAM Types
Types to be discussed
  Synchronous DRAM (SDRAM)
  Double Data Rate SDRAM (DDR SDRAM)
  RAMBUS® DRAM (RDRAM)
Justification for effectiveness of these types
  DRAM often used as a part of a memory hierarchy (Detail discussed in Computer Architecture)
  Reads from DRAM bring data into lower levels of the hierarchy
  Transfers from DRAM involve multiple consecutively addressed words
  Many words are internally read within the DRAM ICs using a single row address and captured within the memory
  This read involves a fairly long delay
Notes: DDR在时钟的上升沿和下降沿都可以进行操作

## Slide 37: DRAM Types (continued)
Justification for effectiveness of these types (continued)
  These words are then transferred out over the memory data bus using a series of clocked transfers
  These transfers have a low delay, so several can be done in a short time
  The column address is captured and used by a synchronous counter within the DRAM to provide consecutive column addresses for the transfers
burst read – the resulting multiple word read from consecutive addresses

## Slide 38: Synchronous DRAM
Transfers to and from the DRAM are synchronize with a clock
Synchronous registers appear on:
  Address input
  Data input
  Data output
Column address counter
  for addressing internal data to be transferred on each clock cycle
  beginning with the column address counts up to column address + burst size – 1

## Slide 39: Synchronous DRAM - burst size=4

## Slide 40: Synchronous DRAM
Example: Memory data path width: 1 word = 4 bytes Burst size: 8 words = 32 bytes Memory clock frequency: 5 ns Latency time (from application of row address until first word available): 4 clock cycles Read cycle time: (4 + 8) x 5 ns = 60 ns Memory Bandwidth: 32/(60 x 10-9) = 533 Mbytes/sec

## Slide 41: Double Data Rate Synchronous DRAM
Transfers data on both edges of the clock
Provides a transfer rate of 2 data words per clock cycle
Example: Same as for synchronous DRAM
  Read cycle time = 60 ns
  Memory Bandwidth: (2 x 32)/(60 x 10-9) = 1.066 Gbytes/sec

## Slide 42: DDR3 For SWORD：MT41J128M16JT
Package：96-Ball FBGA
MT41J128M16

## Slide 43: DDR3 For SWORD：MT41J128M16JT
231(128M×16bit=227+4bit)memory Cell，8 BANK，there are 17 address line
A13~A0
A9~A0
BA2~BA0
214=16384
128×128=27×27
27=23×24
=24
23BANK
214=row
23
128/27Column
Word=16bit
227=128M Word
17位
Notes: 231(128M×16bit=227+4bit)个存储单元(Cell)，分成8个BANK，共有17根地址线。地址线作为行地址输入时分为二组，其中A13~A0控制行阵列选择(8个128×128二维单元)和BA2~BA0控制BANK选择，由RAS控制信号锁存；地址线作为列地址时只用了10根列地址线(A9~A0)，也分为二组，由CAS信号控制锁存)。
每一个BANK由16384(214)个128×128的二维Cell阵列构成，由14根行地址线A13~A0选择，形成由228个Cell组成的三维立体阵列（16384×128×128），共有8个三维立体阵列(BANK)，由行地址线BA2~BA0选择，芯片内部阵列总计231个Cell。
行地址A13~A0每次选中所有BANK中的一个二维Cell阵列(128×128)，并由BA2~BA0选用其中的一个128×128Cell阵列。选中的二维阵列由列地址A9~A3选中其中的一列(128Cell)，与FIFO读缓冲器或数据接口模块连接。若是读操作，读出到FIFO读缓冲器，再由列地址A2~A0控制每次输出16位；若是写操作，从128位输入接口模块选择16位写入。

## Slide 44: MT41J128M16JT Logical Structure
231(128M×16bit=227+4bit)个存储单元(Cell)，分成8个BANK，共有17根地址线。
地址线作为行地址输入时分为二组，其中A13~A0控制行阵列选择，BA2~BA0控制BANK选择，由RAS控制信号锁存；地址线作为列地址时只用了10根列地址线(A9~A0)，也分为二组，由CAS信号控制锁存。
每一个BANK是由228个Cell组成的三维立体阵列16384(214)×128×128，共有8个三维立体阵列(BANK)，芯片内部阵列总计231个Cell。
行地址A13~A0每次选中所有BANK中的一个128×128Cell阵列，并由BA2~BA0选用某个BANK的一个128×128Cell阵列。
选中的128×128Cell阵列由列地址A9~A3选中其中的一列(128Cell)，与FIFO读缓冲器或数据接口模块连接。若是读操作，读出到FIFO读缓冲器，再由列地址A2~A0控制每次输出16位；若是写操作，从128位输入接口模块选择16位写入。

## Slide 45: SWORD Onboard memory-DDR3
Memory Organization
  MT41J128M16JT×2 for 128M×32bit(512MB)
读写时序更复杂请查阅手册

## Slide 46: RAMBUS DRAM (RDRAM)
Uses a packet-based bus for interaction between the RDRAM ICs and the memory bus to the processor
The bus consists of:
  A 3-bit row address bus
  A 5-bit column address bus
  A 16 or 18-bit (for error correction) data bus
The bus is synchronous and transfers on both edges of the clock
Packets are 4-clock cycles long giving 8 transfers per packet representing:
  A 12-bit row address packet
  A 20-bit column address packet
  A 128 or 144-bit data packet
Multiple memory banks are used to permit concurrent memory accesses with different row addresses
The electronic design is sophisticated permitting very fast clock speeds

## Slide 47: Arrays of DRAM Integrated Circuits
Similar to arrays of SRAM ICs, but there are differences typically handled by an IC called a DRAM controller:
  Separation of the address into row address and column address and timing their application
  Providing RAS and CAS and timing their application
  Performing refresh operations at required intervals
  Providing status signals to the rest of the system (e.g., indicating whether or not the memory is active or is busy performing refresh)

## Slide 48: Assignments
7-1、7-4、7-5、7-8